BOMBAS DE VACIO IVYMEN

ZX-1B Ref. 5900620

2XZ-1G Ref. 5900621

Comportamiento de Funcionamiento

Estas bombas al empezar a funcionar producen un poco de humo, después se intensifica y al final, cuando se logra un vacío completo, deja de hacer humo.

Si la instalación donde está conectada (depósito, tubería, etc) tiene una fuga y no se logra un vacío completo, la bomba no dejará de producir humo.

La mezcla de aire con el aceite de la bomba origina una condensación (microgotas) que se expulsa por el tapón de salida de gases, produciéndose una pérdida de aceite al exterior. Hay que vigilar siempre que el nivel sea el correcto.

OBSERVACIONES:

- Para comprobar si una bomba funciona correctamente, tapar con el dedo el orificio de extracción / succión y la bomba no tiene que sacar humo ni aceite por el tapón de salida de gases.

- Todas las bombas de vacío que son de aceite generan humo hacia el exterior mientras no se consigue el vació absoluto.

- Es muy importante colocar filtros y/o trampas para evitar que la bomba al succionar arrastre sustancias hacia el interior y deterioren las paletas y juntas.

ROTARY VANE VACUUM PUMPS

ZX-1B Ref. 5900620

2XZ-1G Ref. 5900621

Operation Behaviour

These pumps to start working produce some smoke, then intensified and at the end when a complete vacuum is achieved, stop making smoke.

If the upgrade is on (tank, piping, etc.) has a leak and not a complete vacuum is achieved, the pump will not produce smoke.

The mixture of air with the oil pump creates a condensation (droplets) which is expelled by the gas outlet plug, resulting in a loss of oil to the outside. Should be monitored whenever the level is correct.

COMMENTS:

1. To check whether a pump is working properly, cover with finger hole extraction / suction pump and not have to remove smoke and oil from the exhaust cap.

2. All vacuum pumps are oil generated smoke to the outside until it gets poured all.

3. It is very important to place filters and / or traps to prevent the pump from sucking drag substances inwards and the vanes and seals deteriorate.